## Slide 1: The Evolution of the Data Center
Albert Puig Artola
apuig@aristanetworks.com

## Slide 2: Arista Networks – Corporate Overview
  Software Designed Cloud Networking
  Founded in 2004
  > 2000 clients of all sizes
  > 600 employees
  Profitable, self-financed, pre-IPO
  A generation ahead in software architecture
Andy Bechtolsheim
President & CEO
Jayshree Ullal
Chairman & CDO

## Slide 3: Data Center Transport

## Slide 4: Data Centre Transport
Agreement on the Physical topology
    Physical Architecture CLOS Leaf/Spine
    Consistent any-to-any latency/throughput
    Consistent performance for all racks
    Fully non-block architecture if required
    Simple scaling of new racks
Spine Layer
10Gbe/40Gbe
Layer 2/3
Leaf layer
10Gbe/1Gbe
Layer 2/3
For the East to West Traffic workflows
  Consistent performance, subscription and latency between all racks
  Consistent performance and latency with scale
  Architecture built for any-to-any Data center traffic workflows

## Slide 5: Data Centre Transport
Active-active L2 topologies possible without new protocols
  MLAG, uses known and trusted standard LACP protocol.
  Achieved without new hardware or any new operational challenges
  But at large scale same challenges as the new protocols, VLANs and MAC explosion
  Layer 2 can scale to a level without requiring new protocols and hardware
Layer 2 Leaf-Spine – MLAG Design
The layer 2 approach only targets the VMobility challenge, what about Scale,
Multi-tenancy, Simplicity and Big Data environments

## Slide 6: Data Centre Transport
To provide scale evolution is to decouple the virtualized network from the physical infrastructure
  Remove the scaling and architecture requirements from the physical infrastructure
  Architecture of the physical infrastructure not tied to the virtual infrastructure
  Building a physical transport infrastructure for bandwidth, port scale and operation
  Allowing the standardize of the the networking platform regardless of the application
Virtualized
Solution
Single scalable
Physical
Infrastructure
Web 2.0
Big Data
Cloud Network

## Slide 7: Data Centre Transport
Building the Layer 3 network
  For scale and East to West traffic growth
  Physical CLOS leaf/Spine architecture
  Standard routing Protocols between the leaf and Spine (OSPF/BGP)
  Equal Cost Multi-Pathing (ECMP) for active-active forwarding
  Standard protocols and Standard hardware,
  No increase in management or operational cost, minimal risk
Increased Resilience
  All links are active, and forwarding traffic
  Distributed failure domain, with multiple spine topology
Subnet-A
Subnet-B
Subnet-C
Subnet-D
Subnet-E
Subnet-F
ECMP
ECMP
Layer 3
between
Leaf and Spine
Layer 2
within
the Rack
OSPF or
BGP
L2/L3 switch
1U or chassis
L3 switch
Scaling a Layer 3 network for East to West traffic
Physically Distributed resilient Core

## Slide 8: Data Centre Transport
The Layer 3 ECMP approach for the IP Transport
  Provides horizontal scale for the growth in East-to-West Traffic
  Provides the port density scale using tried and well-known protocols and management tools
  Doesn’t require an upheaval in infrastructure or operational costs.
  Removes VLAN scaling issues, controls broadcast and fault domains
Overlay Networks are the solution to v-mobility problem
    Abstract the virtual environment form the physical environment
    Layer 3 physical infrastructure for transport/BW between leaf and Spine nodes
    Overlay network virtualizes the connectivity between the end nodes
    Minimize the operational and scale challenges from the IP Fabric Core

## Slide 9: Software is the Key for SDN

## Slide 10: Introducing EOS - the Extensible Operating System
Unique EOS SysDB
  Decouples protocol state from processing increasing reliability
Database for IPC
  Stateless model reduces complexity and improves performance
Live Patching
  Avoid costly downtime for critical security fixes
Linux Kernel
  Open to flexible automation using Linux toolsets and scripts
EOS APIs
  Network wide automation of operations and provisioning systems
Linux Kernel
Leading the next wave of Networking: Software Defined Cloud Networking

## Slide 11
Protected OS Kernel
sysDB
CLI
vSwitch Mgmt
OSPF
STP
LAG
XML/ SOAP
SNMP
ASIC Drivers
3rd Party SW
  Fully modular, multi-process, multi-threaded, stateful restart
  Core sysdb for all session state and inter-process communications
  In-service-software-upgrades
  Extensible architecture enables 3rd party applications
  Focused on making operations simpler
  One system image for all product families
EOS – Extensible Operating System

## Slide 12: Overlay Networks

## Slide 13: Overlay Network
What is an Overlay Network
  Abstracts the virtualized environment form the physical topology
  Constructs L2 tunnels across the physical infrastructure
  Tunnels provide connectivity between physical and virtual end-points
Physical Infrastructure
  Transparent to the overlay technology
  Allows the building of L3 infrastructure
  Physical provide the bandwidth and scale for the communication
  Removes the scaling constraints of the physical from the virtual
Physical
Infrastructure
Overlay
network
Logical tunnels across
the physical Infrastructure

## Slide 14: Overlay Network
Virtual eXtensible LAN (VXLAN)
      IETF framework proposal, co-authored by Arista, Vmware, Cisco, Citrix, Red hat and Broadcom
Vmotion across L3 boundaries
    Transparent to the physical IP fabric
    Provides Layer 2 scale across the Layer 3 IP fabric
    Abstracts the Virtual connectivity from the physical IP infrastruture
Subnet A
VM mobility
Across Layer 3 subnets
VM-1
10.10.10.1/24
VM-2
20.20.20.1/24
VM-3
10.10.10.2/24
VM-4
20.20.20.1/24
ESX host
ESX host
IP Overlay
Subnet B
Subnet A

## Slide 15: Overlay Network
VTEP
VTEP
VTEP
Subnet
10.10.10.0/24
VTEP
Subnet
10.10.20.0/24
VTEP
10.10.10.1
VTEP
10.10.20.1
VTEP
10.10.30.1/32
VTEP
10.10.40.1
Spine1 routing table
10.10.10.0/24  ToR1
10.10.20.0/24  ToR2
10.10.30.1/32  ToR3
10.10.40.1/32  ToR4
Hardware VTEP announce
only the loopback in OSPF
VLAN 10
192.168.10.4
VLAN 10
192.168.10.5
VLAN 20
192.168.20.4
VLAN 20
192.168.20.5
VLAN 20
192.168.20.6
VLAN 10
192.168.10.6
VLAN 200
192.168.20.7
VLAN 100
192.168.10.6
VLAN 10
192.168.10.9
VNI-300
ECMP
Default Gateway for
Physical servers
VRF-1
VRF-2
VNI-200
VNI-100
VNI-200
Virtual Servers
Virtual Servers
Physical Server
(Bare Metal Server)
VLAN translation on VTEP
Tenant DGW
Tenant DGW
With a Layer 2 only Service the Tenant Networks are abstracted from the IP Fabric, SP cloud model

## Slide 16: Overlay Network
Overlay Network provides transparency
  Scalable Layer 2 services across a layer 3 transport
  Decouples the requirements of the Virtualized from the constraints of the physical network
  Tenant network transparent to the transport for Layer 3 scale
  Multi-Tenancy with 24-bit tenancy ID and overlapping VLANs
  Network becomes a flexible bandwidth platform
Physical
Infrastructure
Overlay
network
VNI 2000
VNI 3000
VNI 3000
Layer 3
Transport
Transparent
L2 Services
Scalable, multi-tenant Layer 2 services transparent to the Layer 3 transport network

## Slide 17: Telemetry

## Slide 18: Arista Network Telemetry - Application Infrastructure
Link infrastructure and application
  Critical real-time information enabling network aware applications
Gain Precision Visibility
Utilize differentiated tools
  Close partnerships deliver best of breed solutions
Proactively detect issues
  React to coordinate actions or take direction from other applications / infrastructure
  Notify other elements or operations team of changing conditions
Discrete
Storage
Bare Metal
VMware NSX
Monitoring

## Slide 19
LANZ provides real-time congestion management (streaming)
Path Tracer actively monitor of topology-wide health
Flexible hardware enables Tap Aggregation for a cost-effective solution (filtering and manipulation, GUI)
PTP for time accuracy (10ns)
Timestamping in Hardware for Tap Agg or SPAN / monitor traffic
TCPDump of data-plane and control-plane traffic
Splunk forwarder integration, sFlow
VM Tracer rapidly identify virtual connectivity (VM, VXLAN)
Arista Telemetry for Monitoring & Visibility

## Slide 20
How do we get from this ….

## Slide 21: To this ..

## Slide 22: Software Defined Networking

## Slide 23: Software Defined Networking
Arista Open command API
  Programmatic access to all CLI system configuration & status
  Response is a structured JSON object
  For remote automation/scripting Syntax is sent using JSON-RPC over HTTPS/HTTP
  CLI is now built on top of EOS API
  API calls can done locally on the switch for scripting based on structured JSON
{
"jsonrpc": "2.0", "method": "runCli“, "params": {
"cmds": [ "show interface Ethernet3“, ],
"format": "json" },
"id": 1
}
Request
Response
{ "jsonrpc": "2.0”, "result": [
{ "Ethernet3" :
{ 'bandwidth': 10000000, 'description': '',
'interfaceStatus': 'up’,
}
}
],
“id”: 1
}
vEOS code available for demonstration and testing

## Slide 24: Software Defined Networking
Open to Many Controllers & Programming Models
OpenFlow support with all major controllers
Openstack support. Contribution to Quantum
Network orchestration
Native integration of Vmware vCloud et NSX – VXLAN.
Native integration of Microsoft OMI
Native API instructions developed with key partners, allowing network automation, controlled by applications or services

## Slide 25
10.0.0.0/24
VTEP
VNI 5001
VTEP
VNI 5001
51.51.51.0
VTEP Hardware
Virtualise :
- Network appliances
- Storage
- Servers
Lost Service
ID | Address | On/ Off
7 | 10.0.0.7 | 
6 | 10.0.0.6 | 
5 | 10.0.0.5 | 
4 | 10.0.0.4 | 
3 | 10.0.0.3 | 
2 | 10.0.0.2 | 
1 | 10.0.0.1 | 



Arista EOS and Load Balancers

## Slide 26: Smart System Upgrade: Initiating Maintenance Mode
Virtualization
Load Balancer
Maintenance Mode initiated
Snapshot – stores #neighbors, peers, etc
Network Applications: Smart System Upgrade

## Slide 27: Smart System Upgrade: Initiating Maintenance Mode
Virtualization
Maintenance Mode initiated
Snapshot – stores #neighbors, peers, etc
Directly-connected Vmware hosts put into maintenance mode
Load Balancer VIP Aging enabled via iControl
Load Balancer
Network Applications: Smart System Upgrade

## Slide 28: Smart System Upgrade: Initiating Maintenance Mode
Virtualization
Maintenance Mode initiated
Snapshot – stores #neighbors, peers, etc
Directly-connected Vmware hosts put into maintenance mode
Load Balancer VIP Aging enabled via iControl
Open protocols used to drain traffic
Load Balancer
Network Applications: Smart System Upgrade

## Slide 29: Smart System Upgrade: General Operation
Virtualization
Workload is moved
Overlay facilitates virtual re-cabling
Load Balancer
Network Applications: Smart System Upgrade

## Slide 30: Smart System Upgrade: General Operation
Virtualization
Workload is moved
Overlay facilitates virtual re-cabling
Maintenance is performed on device
Device brought back into service
API calls inform other devices
Load Balancer

## Slide 31: Smart System Upgrade: General Operation
Virtualization
Workload is moved
Overlay facilitates virtual re-cabling
Maintenance summary sent to operations team
Health checks are performed
Removed from maintenance mode
Workloads are rebalanced
Maintenance is performed on device
Device brought back into service
API calls inform other devices
Load Balancer
Network Applications: Smart System Upgrade

## Slide 32: Questions?